## Slide 1
Prototyping Delay-Aware
V2X Safe Communications
Hyunjae Lee
Jihun Lim

## Slide 2
Contents
1
1st week
Setting up the environments we are working on
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
3
3rd week
Designing how to evaluate and analyze performances
4
Feedback & Plans

## Slide 3
1
1st week
Setting up the environments we are working on

## Slide 4
1
1st week
Setting up the environments we are working on
Host machine
Board
CPU Model name:
Intel(R) Core(TM) i5-2400 CPU @ 3.10GHz
CPU(s) : 4
Architecture : x86_64
RAM : 8GiB System Memory
4GiB DIMM DDR3 Synchronous 1333 MHz
4GiB DIMM DDR3 Synchronous 1333 MHz
HardDisk : 500GB ST500DM002-1BD14
OS : Linux msdebian-pc 4.9.0-8-amd64
#1 SMP Debian 4.9.130-2(2018-10-27) x86_64 GNU/Linux
Network card info :
description: Ethernet interface product: I211 Gigabit Network Connection vendor: Intel Corporation serial: 00:0d:b9:4c:c1:5c size: 1Gbit/s capacity: 1Gbit/s width: 32 bits clock: 33MHz

## Slide 5
1
1st week
Setting up the environments we are working on
We have two different kernels on the board
4.9.0-8-amd64 : Volunteer (Original one)
: 5.9 GHz + RT
2. 4.9.0-8-rc8-rt+ : Real time
: 5.9 GHz + RT

## Slide 6
1
1st week
Setting up the environments we are working on
We created 3rd kernel for this specific model
4.9.0-8-amd64 : Volunteer (Original one)
: 5.9 GHz + RT
2. 4.9.0-8-rc8-rt+ : Real time
: 5.9 GHz + RT
3. 4.9.0-8-rc8-rt+ : Volunteer + 802.11p patched
: 5.9 GHz + RT

## Slide 7
1
1st week
Setting up the environments we are working on
3. 4.9.0-8-rc8-rt+ : Volunteer + 802.11p patched
: 5.9 GHz + RT
First, we extracted the configuration file in the board to the host machine.
Then, we applied 802.11p patch and changed some configurations.
: Three features are revised
& in network support, check nl80211
& in network support, check mac option and check OCB
& in kernel hacking, uncheck bug reporting

## Slide 8
1
1st week
Setting up the environments we are working on
Then, we transferred the kernel to the board
~/Kernel/linux $ make INSTALL_MOD_STRIP=1 modules_install
* Notable command
It let the compiled file be compressed without debug files
so that the size of .tgz file became small.
All detailed procedures are listed in the file

## Slide 9
2
2nd week
Understanding basic Linux (Kernels, Network and so on)

## Slide 10
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Network
Linux and Kernel
Scheduling

## Slide 11
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Linux and Kernels

## Slide 12
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Kernel preemption models
Voluntary Kernel Preemption
Fully Preemptible Kernel (Real time)

## Slide 13
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Voluntary Kernel Preemption
The choice of preemption model is a balance
between responsiveness (latency) and
scheduler overhead.

## Slide 14
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Voluntary Kernel Preemption
Lower latency requires more frequent
opportunities for task switches which results
in higher overhead

## Slide 15
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
2. Fully Preemptible Kernel (Real time)
Real-time model is not only additional
preemption models as they also add a number of
modifications that further improve
the worst-case latency.

## Slide 16
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Scheduling under Linux
Focusing on..
1. SCHED_FIFO
2. SCHED_RR
3. SCHED_OTHER

## Slide 17
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Scheduling under Linux
SCHED_FIFO:
Static priority > 0 : it when SCHED_FIFO threads becomes runnable,
it will always immediately preempt any currently running other threads
by being run through other policies.
No time slicing

## Slide 18
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Scheduling under Linux
SCHED_RR:
A simple adaptation of SCHED_FIFO for lower priority activities.
Each thread is allowed to run only for a maximum time quantum.

## Slide 19
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Scheduling under Linux
In a real-time Linux,
the SCHED_FIFO and SCHED_RR behaviors are more efficient
because of the use of a fully preemptible kernel.

## Slide 20
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Network

## Slide 21
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
WLAN : Wireless local area network
Virtual interface and monitor
Virtual access point
Wireless distribution system
Ad-hoc
Infra
structure
Mesh
OCB :
Outside context of a BSS

## Slide 22
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Linux Kernel
Module
Moduler Architecture
Module
In Moduler Architecture,
We can plug and unplug the modules
That we want to use or not to use

## Slide 23
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Linux Kernel
Module
To use modules in Linux,
We have to follow below steps
Install module
Configure module
Use module

## Slide 24
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
1
2
3
To use modules in Linux,
We have to follow below steps
Install module
Configure module
Use module

## Slide 25
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
<the WLAN environment>

## Slide 26
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Linux Kernel
WLAN
(ath9k)
To use WLAN(ath9k) in linux,
We have to follow below steps
Install module
  - built-in module
Configure module
Use module

## Slide 27
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
To use WLAN(ath9k) in linux,
We have to follow below step
Install module
  - built-in module
Configure module
Use module
2
3

## Slide 28
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
<Configure module>

## Slide 29
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
In Configure module part,
Nl80211
Cfg80211
Mac80211
Ath9k

## Slide 30
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
cfg80211
Device registration
Regularity enforcement
Station management
Key management
Mesh management
Virtual interface management
Scanning

## Slide 31
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
cfg80211
Device registration
Registration the device
saving the environment variables
(Band, Channel, Bit rate, High throughput capabilities, Supported interface modes …)

## Slide 32
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
cfg80211
Regularity enforcement
Ensure during the registration of cfg80211
That only the specified frequency channels permitted
For that given country will be enabled

## Slide 33
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
nl80211
cfg80211
User
Nl80211 have roles
to help user and cfg80211 to communicate

## Slide 34
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
<Use module>

## Slide 35
Protocol module
The developer can access
to modify the code in the area
Hardware Dependant module
The access is not easy
to modify the code in the area
SoftMAC
(mac80211)
Hardware Dependant
(ath9k)
2
2nd week
Understanding basic Linux (Kernels, Network and so on)

## Slide 36
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Mac 80211’s roles
Change the format to 802.11
Add the buffer and header according to the Protocol
Send the message to lower layer
Ath9k’s roles
Add the buffer and header
Send the message to hardware
Request interrupt

## Slide 37
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
Mac 80211’s roles
Change the format to 802.3 + LLC
Using the Protocol header, do Decryption and Defragmentation
Send the message to upper layer
Ath9k’s roles
Take the message
Request interrupt
Send the message and status information to upper layer

## Slide 38
3
Designing how to evaluate and analyze performances
3rd week

## Slide 39
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
3
Designing how to evaluate and analyze performances
3rd week
Testing the latency and ),
with different circumstances (kernels, priorities …)
C : worst case execution time
D : relative deadline
T : period

## Slide 40
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
3
Designing how to evaluate and analyze performances
3rd week
Considerations,
Volunteer or Real time kernel
SCHED_OTHER, SCHED_FIFO and SCHED_RR
Different priority
Stressful situation
Testing the latency and ),
with different circumstances (kernels, priorities …)

## Slide 41
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
3
Designing how to evaluate and analyze performances
3rd week
Testing the latency and ),
with different circumstances (kernels, priorities …)
<10 scenarios>
Volunteer
SCHED_OTHER
SCHED_FIFO
SCHED_RR
Lower pr, Higher pr
Lower pr, Higher pr
SCHED_OTHER
SCHED_FIFO
SCHED_RR
Lower pr, Higher pr
Lower pr, Higher pr
Real time

## Slide 42
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
3
Designing how to evaluate and analyze performances
3rd week
Testing the latency and ),
with different circumstances (kernels, priorities …)
Result

## Slide 43
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
3
Designing how to evaluate and analyze performances
3rd week
2. Testing performance with different circumstances

## Slide 44
2
2nd week
Understanding basic Linux (Kernels, Network and so on)
3
Designing how to evaluate and analyze performances
3rd week

## Slide 45
Thank you

## Slide 46
Fully Editable Icon Sets : A
You can Resize without losing quality
You can Change Fill Color &
Line Color
www.allppt.com
FREE
PPT TEMPLATES

## Slide 47
Fully Editable Icon Sets : B
You can Resize without losing quality
You can Change Fill Color &
Line Color
www.allppt.com
FREE
PPT TEMPLATES